## Slide 1: Introduction to signal processing and data analysis for brain research
Rafi Haddad
2021

## Slide 2: Course goals
Provide some of the knowledge and tools required for analyzing different neuroscience related signals & data

## Slide 3: How do we learn? Exercises!
“There is no royal road to mathematics.” (Menaechmus to Alexander the great)

## Slide 4: דרישות הקורס:
  אלגברה ואלגברה לינארית בסיסית
  הסתברות (קצת)
  MATLAB (הרבה)

## Slide 5: חובות הקורס
תרגילים – 30%
מבחן – 70%
תרגילים ניתן להגיש בזוגות
חובה להגיש לפחות 80% מתרגילים
המבחן יכלול שאלות מהתרגילים!
אתר הקורס:https://www.rafi-haddad-lab.info/signal-processing-and-data-analysis

## Slide 6: Books
Signal Processing for Neuroscientists by Wim van Drongelen
Understanding digital signal processing by Richard Lyons
Introduction to Signal Processing by Sphocles J. Orfanidis
Mike X. Cohen - youtube channel

## Slide 7: תוכנית הקורס
  דגימה:
    מה זה אות,
    איך דוגמים אותו,
    איך מערכים את האיכות
    ואיך משפרים את האיכות
  השוואה ועיבוד:
    כיצד משווים בין שתי אותות,
    כיצד מוצאים קשרים בין אותות
  אנליזה מתקדמת:
    ניתוח תדיריות,
    השוואה בין פאזות
    הוצאת מאפינים,
    קלסטרים

## Slide 8: דוגמא לעיבוד אות במדעי המוח

## Slide 9: דוגמא לניסוי במעבדה
אנחנו רוצים להבין איך אנשים נושמים
  בשעות שונות ביום
  ברמת פעילות שונה
  בזמן מחלה
  כשהם אוכלים, מריחים וכו וכו
פיתחנו חיישן קטן ואלחוטי שמשדר לטלפון החכם
שאלות:
  כמה נקודות לקחת בשניה?
  כמה ביטים להקצות לכל נקודה?
  מה כדאי: להעביר את האות כמו שהוא או להפוך אותו לדיגטלי קודם?
  האם כדאי לשמור דטה לוקלי ואז להעביר אותו?
  איזה תדירות נשימות ישנם בהקלטה?

## Slide 10: מציאת קשרים בין נוירונים

## Slide 11: דוגמא: קלספיקציה של סוגי נוירונים
Neuron 1: | || | ||| | | | | | |
Neuron 2: | || | |
Neuron 3: | | | | | | |
Irregular
(Poisson)
Sparse
(Poisson)
Oscillating
Questions:
How can we characterize a neuron type?
How can we quantify the information it contains?
Neuron 4: ||||| ||||| ||||||
Bursting

## Slide 12: נתחיל...

## Slide 13: Definitions
Signal is a detectable physical quantity by which information can be transmitted.
Signal processing is the processing, amplification and interpretation of signals

## Slide 14: Signals & data processing in Neuroscience
אנחנו נתמקד באותות אלקטרופיזיולוגים
אבל השיטות שנלמד מתאימות לכל הטכניקות
לפעמים נראה אפליקציות שאינם קשורות למדעי המוח באופן ישיר

## Slide 15: סוגי אותות: אנלוגי לעומת ודיגטלי
Analog signals – any real world signal
Digital signal – signals stored in a computer

## Slide 16: סוגי סגנלים
סופי \ ואין סופי
מחזורי\ ולא מחזורי
חד ממדי \ רב ממדי (תמונה, סרט)

## Slide 17: דוגמאות לאותות
טמפרטורה
מתח ממברנה
מחזור מכירות של חברה בכל יום
נשימות של תינוק ((baby sense
דופק

## Slide 18: סוגי אותות במוח
  EEG (electroencephalogram)
  Extra and intra cellular recording
  LFP (Local field potential)
  Ecog (electrocorticography)
  Optical imaging
  fMRI, PET
  MEG - Magnetoencephalography

## Slide 19: EEG
Spatial resolution: mm
Time resolution: < ms
EEG recording
Advantages:
  Non-invasive
  Can be performed during behavior
Disadvantages:
  Only surface neurons that are synchronized
  Many artifacts

## Slide 20: Brain disorders:
Herrmann 2005
Notes: Fig. 3. Hypothetical relationship between gamma activity, brain regions
and pathology. Even in healthy subjects, gamma activity shows a
significant interindividual variation that correlates with cognitive parameters.
In ADHD patients, it is slightly higher. For schizophrenia a subgrouping
in positive and negative symptoms is well documented, and it has
been suggested that both groups can be differentiated by increased (positive
symptoms, especially hallucinations) or reduced (negative symptoms)
gamma activity. Alzheimer’s disease is accompanied with a reduction of
gamma synchronization. An extremely high level of gamma activity may
lead to epileptic seizures through the hyper-excitation of the cortex.
Accordingly, states with higher gamma activity contain a risk for such
seizures.

## Slide 21: Extra cellular recording
Spatial resolution: microns
Time resolution: < ms
recording movie
https://www.youtube.com/watch?v=l_Q2iySTEIc
Advantages:
  The real thing…
  Can be done for many days while the animal performs tasks
Disadvantages:
  Only few neurons

## Slide 22: Intra cellular recoding
Spatial resolution: microns
Time resolution: < ms
intra cellular recording
Advantages:
  The real-real thing
Disadvantages:
  Only 1-2 neurons at a time
  Good for 1-2 hours
  Very hard to do during behavior

## Slide 23: LFP – local field potential
Spatial resolution: 100 -300 microns
Time resolution: tens of ms to seconds
The local field potential (LFP) refers to the electric potential in the extracellular space around neurons.

## Slide 24: Optical imaging
Changes in tissue reflectance
Calcium imaging
Dye sensitive
Two photon
Spatial resolution: microns
Time resolution: >50 ms
Advantages:
  Enables recordings of many neurons
Disadvantages:
  Only surface neurons
  Photo-toxicity

## Slide 25: Functional MRI
detecting the changes in blood oxygenation and flow that occur in response to neural activity
Spatial resolution: 1 mm^3
Time resolution: Seconds
Advantages:
  Non-invasive
  During behavior (without movements)
Disadvantages:
  Only neurons that are synchronized
  Many artifacts

## Slide 26: MEG - Magnetoencephalography
Measures small magnetic fields produced in the brain
Spatial resolution: few mm
Time resolution: ms
Advantages:
  Non-invasive
Disadvantages:
  Mostly surface neurons that are synchronized
  Many artifacts

## Slide 27: Neurophysiological signals Summary

## Slide 28: עכשיו באמת נתחיל...
Cite mike X youtube channel
https://www.youtube.com/channel/UCUR_LsXk7IYyueSnXcNextQ

## Slide 29: אות מחזורי
אות הוא מחזורי עם מחזור T אם מתקיים:
דוגמא:

## Slide 30: Sine
sin(x) = Asin(x+2*pi)
Radians to degrees: pi == 180 degree
Let x in radians then x/(2*pi)*360 degrees
Let x in degrees then x/360*2*pi radians
w = 2*pi*f
T = 1/f; f=1/T
y = sin(x); x=[0,2pi]
y = sin(3x); x=[0,2pi]
y = sin(3*2*pi*t); t=[0,1]
w=2*pi*f
A

## Slide 31: Cosine
cos(x) = cos(x+2*pi)

## Slide 32: Frequency, Period and amplitude

## Slide 33
Signal phase

## Slide 34: Signal phase

## Slide 35: Signal phase

## Slide 36: Sine (https://www.youtube.com/watch?v=9RvZXZ46FRQ&list=PLn0OLiymPak2jxGCbWrcgmXUtt9Lbjj_A&index=3)
SHOW Mike X Cohen VIDEO

## Slide 37: קבוצות של תדיריות
Alpha – 7-13 Hertz
  When we are relaxed
Betha – 12-30 Hertz
  Alert, afraid
Delta – 0.1-5 Hertz
  Unconscious, deep a sleep
Theta - 4-7 Hertz
  Hippocampus
  Olfactory system
Gama – 30-100 Hertz
  Maybe related to cognition (the segregation and binding problems)

## Slide 38: דגימה של סיגנל
Add grid
fs = Sampling rate
Sampling
resolution
1/fs = 1/2 = 0.5

## Slide 39: דגימה של אות
דוגמאות
  Sin(2*pi*t), t=0:0.1:1
    A one hertz cycle
  Sin(2*2*pi*t), t=0:0.1:1
    A two hertz cycle
  Sin(2*3*pi*t+pi/2), t=0:0.1:1
    A three hertz cycle shifted by pi/2 (e.g. a cosine)
    Example: plot(t,x) for plotting 1 second
    And t=0:0.1:2 for plotting 2 seconds
  Matlab Examples

## Slide 40: Sampling
כיצד כדאי לדגום סיגנל?
נגדיל את הקצב של הדגימה?
עד איזה גובה?
מה התשלום?
האם לדגום בקצב זהה?

## Slide 41: Over sampling

## Slide 42
fs = 2
fs = 4
fs = 10
fs = 20
Time (sec)

## Slide 43: The sampling theorem:
If the signal is band-limited. That is, it contains a maximum frequency fmax
The sample rate fs must be chosen at least twice the maximum frequency
  fs > 2fmax
This is called the Nyquist interval
  קצב דגימה טוב: לפחות פי 5 מהתדירות הכי גבוהה

## Slide 44: סיכום (מה למדנו ומה צריך לדעת)
סוגי אותות שונים במוח והרזולוציה שלהם יתרונות וחסרונות
אותות אנלוגים, דיגיטלים ומחזורים
מה זה אליאס ואיך מחשבים את הסיגנל שמקבלים בהתאם לקצב הדגימה שנעשה
משפט הדגימה

## Slide 45: Basic statistics
Mean:
Variance:
Covariance: